Active Yaw planning
Common field of view
Field of view of previous waypoint projected to current waypoint in the yaw plane
Field of view of current frame
Yaw unit circle

---
- Common Field of view factor (c) can be
    - 0 => only exploration
    - 1 => only mapping
    - 0.5 or (0 – 1) => needed for both mapping & exploring

---
- To compute current best yaw
  - Project end points of plane segments visible in previous viewpoint into the yaw circle of current view point => common field of view
  - ‘c’ should be based on
    - Current map
    - Common field of view
    - Velocity direction
  - Based on ‘c’, compute the best yaw
    - Eg: c = 0.5 => previous yaw + (c * 90 deg)

---
Projecting planes to yaw circle